## Slide 1: Report on OpenDaylight (ODL) Plug-in for Padtec ROADMs
Alaelson Jatobá1, Darli Mello1, Christian Esteve Rothenberg2, Dalton S. Arantes1, Sergio Timóteo3
University of Campinas – Unicamp
School of Electrical & Computer Engineering – FEEC
1{alaelson,darli,dalton}@decom.fee.unicamp.br
2{chesteve}@dca.fee.unicamp.br
3{sergio}@padtec.com.br
December 01, 2014.

## Slide 2: Outline
Abstract;
Goals;
SDN System Architecture;
ODL Plug-in implementation;
Padtec NMS API and Architecture;
System Features;
Client Application;
Scenario at Super Computing 2014;
SC14 Results and Team.

## Slide 3: Abstract
This work describes the software developed by Padtec and Unicamp for demonstration at Super Computing 2014 (SC14). The plug-in controls Padtec’s Reconfigurable Optical Add/Drop Multiplexers (ROADMs), providing support to software defined networking (SDN) using the OpenDayLight (ODL) controller. The main achievement was a peak rate of 1.55 Tbps provisioned using a third-part client application that sends commands to the ODL controller, increasing and decreasing the bandwidth as needed.

## Slide 4: Goals
Maximize the wavelength utilization;
Reduces the blocking probability;
Assign appropriate routes and wavelengths over the lightpaths to maximize throughput;
Manage lightpath establishment in real-time;
Provisioning resources on demand (Manage connection request).

## Slide 5: SDN System Architecture
SB Unicamp Plug-in
Orchestration
NB Caltech Plug-in
OpenFlow Support
Console Client
Rest
Caltech Fast Data Transfer
ODL NB Interface
Rest
PADTEC ROADM
Rest
Padtec
Protocol
NB RESTful API
Padtec Mgmt Software
Rest
OpenFlow
Switch

## Slide 6: Implementation ODL Plug-in
Implemented by the Unicamp team based on Padtec NMS RESTFul APIs, abstracting the hardware complexity features of the ROADM device;
Offers to the user two simple methods (increaseBandwidth and decreaseBandwidth). Channel selection and other messages of Padtec’s management software are not exposed to the user;
Works as an OpenDayLight plug-in providing SDN programmability and orchestration to Padtec’s devices.

## Slide 7: ODL Plug-in
Features:
Acts as a South Bound interface in the OpenDayLight;
Implements the RESTFul API to control the Padtec ROADMs;
Keeps a memory of the connection states;
Keeps a route table;
Implements the first-fit algorithm in order to choose the lambda to provision and remove channels;

## Slide 8: ODL Plug-in
It is composed of two parts:
South Bound (SB): implements the required logic to use Padtec APIs and provides useful abstractions;
North Bound (NB): is a RESTFul interface to receive command from the clients.
  Implemented by Caltech Team.

## Slide 9: ODL Plug-in: Interaction with the client application
A RESTful North Bound Interface is used to integrate the client apps with the SDN controller.
Supported Commands:
  useCache: is a boolean value to set if the cache memory and route table must be used;
  increaseBandwidch – activates a channel between two nodes;
  decreaseBandwidch – removes a channel between two nodes;
  useExtreme: is a boolean value to set the Extreme switch to be used in Caltech Booth. It was a temporary feature developed during SC14.
  getTopology: returns the network topology.
  getNEs: returns the information about the network elements.

## Slide 10: ODL Plug-in: Methods to increase and to decrease bandwidth
Increases the bandwidth between source and destination nodes;
To increase bandwidth, the channel is chosen using the first-fit algorithm in descending order, but to decrease bandwidth the algorithm uses the ascending order of channels;
If the client sets the cache memory on, the routes are fetched from cache, improving the performance of the system by reducing the amount of queries to get the routes from the Padtec´s Management Software through the RESTful APIs.

## Slide 11: ODL Plug-in INCREASE BANDWIDTH
CLIENT
NB
REST COMMAND
START
Accept?
call method
yes
Use Cache?
no
cache
yes
Route from src to dst
Send get routes cmd to PADTEC Mgmt
Select channel from descending order
save
return
return
Make create-occupation JSON
Send command
to Padtec Mgmt
confirm?
no
FAIL
yes
SUCCESS
no

## Slide 12: ODL Plug-in DECREASE BANDWIDTH
CLIENT
NB
REST COMMAND
START
Accept?
call method
yes
Use Cache?
no
cache
yes
Route from src to dst
Send get routes cmd to PADTEC Mgmt
Select channel from ascending order
return
return
Make remove-occupation JSON
Send command
to Padtec Mgmt
confirm?
no
FAIL
yes
SUCCESS
no
save

## Slide 13: Padtec RESTful Architecture
SB Unicamp Plug-in
Orchestration
NB Caltech Plug-in
OpenFlow Support
ODL NB Interface
PADTEC ROADM
Rest
Padtec
Protocol
NB RESTful API
Tomcat Web Server
Padtec Mgmt Software
RMI
REST Interface API Features:
Topology Search;
ROADM Discovery;
CrossConect Traceability;
Paths Discovery and Monitoring;
Path Configuration;

## Slide 14: Padtec RESTful North Bound API
Commands:
  GET $SERVER_ROOT/rest/nes
  GET $SERVER_ROOT/rest/ne-interface/$NE_ID
  GET $SERVER_ROOT/rest/cossconnections/$NE_ID
  GET $SERVER_ROOT/rest/topology
  GET $SERVER_ROOT/rest/routes/$SOURCE_ID/$DESTINATION_ID
  POST $SERVER_ROOT/rest/create-occupation/$SOURCE_ID/$DESTINATION_ID
  POST $SERVER_ROOT/rest/remove/$SOURCE_ID/$DESTINATION_ID

## Slide 15: System Features
Use network at full speed;
Dynamically monitoring the capability of the storage systems;
Dynamically monitoring the network path in real-time;
Dynamic Distributed Service Architecture;
Integration of existing monitoring tools (via APIs);
Routing and Wavelength Assignment (RWA).

## Slide 16: Client Application
FDT - Fast Data Transfer from Server to Storage System;
Lightpath management;
Preventive network diagnosis;
Reads and writes coordinated, streams or a large set of files with smooth data flow across long-range networks;
  Science programs handling hundreds of petabytes per year

## Slide 17: Super Computing 2014

## Slide 18: SC14 Complete overview

## Slide 19: SC14 Complete overview

## Slide 20: Network Interfaces used in the Showfloor
3 Booths in the showfloor:
  Caltech: 10 x 100 Gbps
  iCAIR: 6 x 100 Gbps
  Vanderbilt: 4 x 100Gbps
Caltech booth has 2 switches
  1 Brocade with 4 x 100Gbps
  1 Extreme with 6 x 100Gbps

## Slide 21: SC14 Demo Topology

## Slide 22: Padtec Directionless ROADM
4 Boards 100G OTU-4
C21 a C24
Direction A
Direction A
Direction B
Direction B
Direction B
10 Boards 100G OTU-4
C21 to C30
Direction A
10 Boards 100G OTU-4
C21 a C30
Direction C
Direction C
Direction C

## Slide 23: SC14 Demo Topology

## Slide 24: Directionless Interconnections
Direction B
Direction C
Direction A
DEMUX
MUX
Site 1
Site 2, Direction A
Site 3, Direction B
Line IN
Line OUT
IN/OUT
IN/OUT
IN/OUT
IN/OUT
IN/OUT
IN/OUT
Line IN
Line OUT
Line IN
Line OUT

## Slide 25: Management of SC14
RoadMap :
NE Features and constraints modeled in YANG, using Padtec YANG model
NE mode changed via Software Upgrade/Downgrade
Padtec NMS
GUI
PPM3
CLI
Network Elements (NMSN mode)
Controller API
(OpenDaylight)
REST

## Slide 26: Super Computing 2014 Results

## Slide 27: SC14 Demo Results by Prof. Harvey Newman
We sustained 1.4 Tbps during our memory to memory warmups on the first day. The peak was 1.55 Tbps in and out of the Caltech booth. During the warm up we also had 1 Echostreams server doing a total of > 150G in and out of its two Mellanox NICs simultaneously. Disk to memory we reached a peak of 1.01 Tbps, reaching our goal. We have been able to sustain 940+ for long periods.
We sent and received 11 Petabytes of data to and from the Caltech booth. 3.7 Petabytes went over the wide area between New Orleans and Caltech, Victoria, Michigan, Sao Paulo and NERSC.
We had sustained flows of very close to 100G in one direction from UVic; and large flows often making up a big fraction of 100G to and/or from Caltech, UMich, and Sao Paulo. There were also new disk to disk and memory to memory records between the Northern and Southern hemispheres.
In terms of wide area traffic rates, we reached 370G sustained, and 310G for a long time, with a solid 100G (99.74G to UVic), up to 100G from Umich, and up to 93G from Caltech, 92.5G from the combination of CERN and Sao Paulo (via FLR), and 45G from NERSC.
Disk to disk was harder, because of problems which might have been due to the OS and/or what happens when you hit the CPUs as hard as we did. Nevertheless, we reached a peak of 340 Gbps peak and 300 Gbps sustained disk to disk. We will continue to investigate further and resolve the issues with the OS and/or with the controller, CPUs or other potential issues.
A lot was learned in terms of putting PhEDEx into larger scale use with circuits, and achieving more deterministic workflow in the large scale. Work on some of the built-in time delays, and perhaps on the central (single instance) database should continue, as part of getting the new PhEDEx paradigm out in the field.
There were also some successes with OpenDaylight, limited in part by the very short time available and the early state of the ODL Hydrogen release. We will move forward with the ODL controller's reactive mode using our own testbed facilities and our Brocade switches at Caltech and elsewhere.

## Slide 28: Results
sustained 1.4 Tbps during our memory to memory;
peak was 1.55 Tbps;
Disk to memory we reached a peak of 1.01 Tbps;

## Slide 29: Lightwave Online: Padtec demos SDN-controlled directionless ROADM at SC14
Harvey Newman of Caltech, professor of Physics and head of the SC14 team, said, "Padtec ROADMs and software behaved perfectly. Its ROADM and 100-Gbps transponders not only allowed an astounding 1 Tbps of data to flow during SC14 but also demonstrated how an external third-party OpenDaylight controller can be used to reconfigure topology on demand and provision the individual network components.”
Lightwave Online, “Padtec demos SDN-controlled directionless ROADM at SC14”, Nov 25th, 2014, url:
http://www.lightwaveonline.com/articles/2014/11/padtec-demos-sdn-controlled-directionless-roadm-at-sc14.html?cmpid=EnlDailyNovember252014.

## Slide 30: 1.55 Tbps peak rate - memory to memory transfer

## Slide 31: 1 Tbps peak rate – disc to memory transfer

## Slide 32: Load of the channels in the demo

## Slide 33: Performing a command to decrease the bandwidth between nodes 1 and 2
Console Client Log
OpenDayLight Controller Log

## Slide 34: Pictures of the Caltech Booth
Padtec ROADM
Racks with EchoStream and Dell Servers, and
Extreme and Brocade Switches

## Slide 35: Pictures of the iCAIR Booth
Padtec ROADM
And Caltech’s Racks

## Slide 36: Pictures of the Vanderbilt Booth
Padtec ROADM

## Slide 37: SC14 Team